## Slide 1: Thar Sun 100 MWp: deal-desk recommendation
Single-axis tracker quote, margin check, customer value case and Q4 forecast | Manjit Mandal | 24-Oct-2026
Fictional customer and supplier: portfolio project
Notes: Context: one connected deal from customer brief to forecast. All companies fictional. Energy is PVGIS-simulated; costs and pipeline are synthetic assumptions documented in the Assumptions sheet and README.

## Slide 2: Quote at 3% discount: healthy margin, within authority
₹7.86/Wp
Net price (list ₹8.10, −3%)
₹78.6 cr
Contract value (≈ USD 8.27M)
15.6%
Contribution margin (floor 12%, target 18%)
Sales Mgr
Approval level (discount ≤ 3%)
Minimum acceptable price is ₹7.53/Wp, so up to 7.1% discount is possible before breaching the 12% CM floor.
Competitor B offers ₹7.60/Wp. Matching it leaves CM at 12.8%, only 0.8 pts above the floor with no buffer for steel moves.
Hold price and sell value: steel-index clause and an independent yield review instead of further discount.
Fallback: up to 5% discount (CM ≈ 13.9%) with Sales Director approval, in exchange for a 20% advance.
Chart: Price ladder (INR/Wp)
| Min. acceptable (12% CM) | Competitor B offer | Our net price | Customer budget | List price | Customer break-even
INR/Wp | 7.53 | 7.6 | 7.86 | 8 | 8.1 | 10.54
Notes: Source: Quote_Calculator and Sensitivity sheets. Approval matrix: Manager <=3%, Director <=6%, VP <=10%, CFO above or below CM floor.

## Slide 3: The tracker pays back in ~5.5 years for the customer (simulated)
Chart: Monthly yield, kWh per kWp (PVGIS simulated, fictional site)
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Fixed-tilt (PVGIS) | 160.1 | 150.9 | 164.5 | 155.5 | 150.1 | 132.4 | 120.5 | 119.7 | 133.2 | 155.4 | 148.4 | 156.6
Tracker planning case | 164.4 | 165.9 | 193.4 | 197.7 | 203.3 | 178.8 | 153.8 | 145 | 157.4 | 173.8 | 153.3 | 157.2
+17.0% energy
Planning case (PVGIS ideal +24.3%, 70% realised)
₹26.8 cr NPV
Tracker vs fixed-tilt @ 9%; IRR 17.3%
₹10.54/Wp
Break-even tracker price vs our ₹7.86
Our ₹2.57 cr premium over the competitor is recovered by 0.6% extra yield.
Notes: PVGIS models ideal tracking with no backtracking or row shading, so only 70% of the simulated gain is used. A bankable case would use PVsyst with the real layout. Labelled as simulated, not manufacturer performance.

## Slide 4: Steel price, not FX, is the main margin risk on this deal
Chart: Contribution margin % vs steel price change (FX at 94.95)
| −15% | −10% | −5% | 0% | +5% | +10% | +15%
CM % at proposed price | 24.2 | 21.3 | 18.5 | 15.6 | 12.7 | 9.9 | 7
CM floor 12% | 12 | 12 | 12 | 12 | 12 | 12 | 12
About 70% of direct cost (₹4.50 of ₹6.43/Wp) is steel-linked. A +10% steel move takes CM to 9.9%, below the floor.
Imported drives and controllers are about 19% of cost: +₹2.5/USD costs only ≈0.4 pts of CM.
Mitigation: index-linked steel clause (±5% band, 50/50 share), and lock steel purchase within 2 weeks of PO.
FX: hedge the USD content at order. No pass-through needed.
Notes: Source: Sensitivity sheet, Table 1 and Table 2.

## Slide 5: Q4 weighted forecast is $353M, up $23.4M week on week
Chart: Q4-2026 forecast by weekly snapshot (USD m, synthetic)
| 07/03 | 07/10 | 07/17 | 07/24 | 07/31 | 08/07 | 08/14 | 08/21 | 08/28 | 09/04 | 09/11 | 09/18 | 09/25 | 10/02 | 10/09 | 10/16 | 10/23
Weighted forecast | 88.8 | 102.5 | 127.9 | 133.1 | 154.8 | 180 | 189.7 | 202.3 | 227.1 | 245.5 | 265.9 | 288.2 | 312.3 | 324.8 | 337.2 | 329.4 | 352.8
Closed won + Commit | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 15.5 | 15.5 | 15.5 | 53.3 | 69.1 | 145.6 | 187.8 | 234.5 | 263.8
$264M
Floor: Closed + Commit
$353M
Most likely: weighted
$457M
Stretch: + Best Case
Thar Sun ($8.3M) sits in Best Case at Proposal/Quote
Notes: 151 synthetic opportunities in Salesforce (Developer Edition). Weighted = amount x stage probability. Snapshots every Friday.

## Slide 6: Value pitches win about twice as often as price pitches
Chart: Win rate by value proposition (closed deals, synthetic)
| Local manufacturing (n=9) | Lowest capex (n=17) | Fast delivery (n=13) | Energy yield gain (n=30) | Bankability & warranty (n=17)
Win rate % | 11 | 24 | 31 | 47 | 59
Overall win rate 38% on 86 closed deals. Bankability (59%) and energy yield (47%) pitches lead. "Lowest capex" wins 24% at a lower CM.
Price causes 32% of losses and fixed-tilt 23%. Both are answered by the customer value case, not by discount.
Existing customers convert at 64%. Prioritise repeat-customer pipeline and references.
Next: add a loss-reason validation rule in Salesforce, re-test with real data, and track hit rate monthly.
Notes: Small samples per group: directional only. SQL in queries.sql; Excel version in Pipeline_Analytics.xlsx Win_Loss sheet.